Serial Memory rev1.0

Documentation

Document version: 18.02.2010

http://www.network-innovation.de

# General information
## Electrical data
Supply voltage:	4.5V < Vcc < 5.5V
Supply current:	100mA max.

## RS232 parameters
Transfer rate:9600 bit/s
Data bits:	8
Parity:	none
Stop bits:	1
## Memory information
Capacity:	512 bytes
Technology:	EEPROM, non volatile
Write cycles:	approx. 100.000 per cell
# Communication protocol
## General information
Communication is established via a standard compliant RS232 (9600/8/N/1) interface.
The protocol is a plaintext protocol. This implies that no non-readable characters (except newline) are used. You can easily connect to the device with a standard terminal program.
All command-lines have to end with a newline character (0x0A, in this manual identified by ), datafields are separated by a space character (0x20).
Most commands are followed by a checksum before the newline character. See the parameter description for further information.
Hex values have to be given in lowercase, commands in uppercase.

## List of commands
### SET
#### Description
The SET command writes one byte of data to the specified address.
#### Syntax
SET aaa dd cc
Parameter	Description	Valid range
aaa	Address of the memory cell to be written to	0x000 to 0x1ff
dd	Data byte to be written to the memory cell	0x00 to 0xff
xx	Checksum / xx = (aaa + dd) MOD 0x100	0x00 to 0xff

#### Return codes
Return code	Description
aaa dd xx	Command succeeded.
CHECKSUM	Checksum mismatch
ERROR	Syntax error

### GET
#### Description
The GET command reads one byte of data from the specified address.
#### Syntax
GET aaa xx
Parameter	Description	Valid range
aaa	Address of the memory cell to be written to	0x000 to 0x1ff
xx	Checksum / xx = aaa MOD 0x100	0x00 to 0xff

#### Return codes
Return code	Description
aaa dd xx	Command succeeded.
CHECKSUM	Checksum mismatch
ERROR	Syntax error

### MACSET
#### Description
The MACSET command writes a MAC(media access control) address consisting of 6 bytes to the memory.
#### Syntax
MACSET aa:bb:cc:dd:ee:ff xx
Parameter	Description	Valid range
aa to ff	Data bytes of the MAC-address	0x00 to 0xff
xx	Checksum / xx = (aa + bb + cc + dd + ee + ff) MOD 0x100	0x00 to 0xff

#### Return codes
Return code	Description
aa:bb:cc:dd:ee:ff xx	Command succeeded.
CHECKSUM	Checksum mismatch
ERROR	Syntax error

### MACGET
#### Description
The MACGET command retrieves the MAC(media access control) address consisting of 6 bytes from the memory.
#### Syntax
MACGET
#### Return codes
Return code	Description
aa:bb:cc:dd:ee:ff xx	Command succeeded.
CHECKSUM	Checksum mismatch
ERROR	Syntax error

### DUMP
#### Description
The DUMP command sends a hexdump of the whole memory to the serial port.
For debugging purposes.
#### Syntax
DUMP
#### Return codes
The command has no return code. It outputs a table containing the memory contents.
### NOP
#### Description
The NOP command does nothing.
For debugging purposes.
#### Syntax
NOP
#### Return codes
Return code	Description
NOP	Command succeeded, nothing done.